## Slide 1
C
A
B
I think that we should include the current-time series of the events of each bacteria strain shown above (reg. E. Coli/Staph), like we have for the previous PPT presentations labelled D, E & F, but not the full i vs. t series. I think that would be a bit too much. I will also need to make these images smaller (I think?)
F
D
E
Notes: Things that will need to be included in the paper (just my random thoughts).
PET fabricated using the single-track etch method have a negative surface charge (zeta potential: ~ -4 mV).
The polystyrene particles having a slightly negative zeta potential, translocate through the pore electro-osmotically (might need to reflect this with the current time series).
Bacteria cells (E. Coli & Staph) travel electrophoretically through the pore.
In a pore with negative surface charges, electroosmotic flow occurs towards a negatively biased electrode. If the particles are charged, there will also be an electrophoretic force acting on them e.g. electrophoretic force on negatively charged particles will be directed towards a positively biased electrode. With no pressure difference applied, the particles will move in the direction of electrophoresis if their zeta potential is higher than the zeta potential of the pore walls. If the zeta potential of particles is lower than that of the pore walls, the translocation will occur in the direction of electroosmosis i.e. towards a negatively biased electrode.
E. Coli has a much more negative zeta potential than the PET pore walls that we measured. This measured zeta potential is also consistent with literature values of the zeta potential and our experimental findings by which, the bacteria travel in the opposite directionality to the polystyrene particles.